12,000 Open Farm Rules

Rules will be in place for 2015 Season.

- AGE

- Any age of tractor/ 2 wheels / rear wheel drive train only.

- All drivers must be at least 16 years old, with legal proof in their possession.

- All contestants enter at their own risk.

- FUEL – Diesel fuel only

- No nitrous oxide

- No LP

- Water injection allowed.

- NTPA Water & Fuel Rules apply.

- Must have water & fuel sample valves.

- MOTOR – Cylinder, block, head and crankcase factory supplied OEM, OR OEM REPLACEMENT

- Maximum 640 cubic inch allowed.

- Must be stock appearing, for that make and model

- All components will be stock original pieces, or stock/refurbished components that were originally made by the tractor models manufacturer.

- All components must bolt in the original stock location modification.

- Heads will be for that make/model.

- MOTOR RPM LIMITS

- 3250 max.

- Mandatory working governor – will be rpm checked

- TTPA official will pull the throttle for governor/tack checks

- Owner/driver is responsible for the reflective tape to be put on the flywheel or harmonic

- No reflective tape for tach checking is a disqualification

- Must have a tach trigger plug securely mounted near the rear air shut off cable.

- DIESEL FUEL PUMP

- Bosch P-3000 13mm pump

- Must have a 3-way bypass valve mounted before the injection pump operated from seat.

- HOOD, GRILL, FRAME TRANSMISSION, REAR END AXLES, CLUTCHES AND BRAKES

- Must be stock in appearances and dimensions for the make/model

- Homemade front axles allowed.  114” Maximum wheelbase.

- Wide fronts only. Front tires will track within the rear tires.

- Slipper clutch allowed

- Changing of Rear End Gears allowed

- Factory brakes or better.  Must work.

- Three Pt. Hitch is not allowed on the tractor or for rear weight brackets

- Weights must not exceed rearward beyond rear tires vertical edge, and cannot be more than 13 ft. from the centerline of the rear axle to the furthest point forward.

- No differential locks allowed in competition, and must be made inoperable.

- TURBO

- No larger than 3” In & 3” Out (Must follow NTPA Rules & Tech Inspection Rules), unless TTPA board variance is given. (new for 2004)

- No intercoolers.

- Must have two 3/8” bolts in horizontal portion of exhaust pipe.  Bolts must be installed 90° degrees to each other.

- All Turbos will be teched and tagged before the start of the season, along with spot checks throughout the season.

- HITCHES

- Will be factory or better drawbar with a 3” wide and 3-3/4” long opening.  No Clevis.

- Drawbar will be no closer than 18 in. from center of the rear axle to hitching point.

- No vertical supports above centerline of rear axle

- Hitch height is 20”.

- Drawbars to be ridged in all directions

- SAFETY

- Wheelie bars, NTPA/TTPA Guidelines & Rules

- Kill switch must activate the air shut off valves per NTPA/PRO Farm rules, located in an area easily accessed by sled hooker official

- No Steel fans.

- Must have factory appearing fenders

- Must have 200 – lb. movable ballast

- Must wear SFI fire suit, neck brace, gloves, head sock and fire shoes, SFI 3.2A-1

- Must wear full face DOT approved helmet.

- Must have a minimum of 2.5 lb. fire extinguisher with access by the driver.

- Must have a roll cage & tie bars (Built to SFI specs.) 5 pt harness and detachable steering wheel.

- Front Skis per NTPA Specs.

- Must have 2 reverse lights.  One in dash and at rear of tractor center or above the hitch.

- Front Balancer must have 360° shielding.

- All tractors must have side shields.

- Tractors with fiberglass hoods need minimum .090 aluminum inner side shielding and minimum .090 aluminum turbo shroud.

- TIRES/RIMS – front and rear – Aluminum rims allowed.

- Rear – Tire size maximum of 24.5 on a 32” rim, 20.8 on 42” rim, or 18.4 on a 46” rim. Any cut, bias or radial tire.

- All rules will be for 2 years, with conditions that the TTPA board may alter for safety and fair play.

- All General Rules Apply.

_____________________________________________________________________________________________

Revisions:

November 2003 – TTPA Turbo Rule Approved and instated by Board

February 2004 – TTPA board approved Slipper Clutch. Top Cut Tires & Non-OEM Gears for rear End

March 2004 – TTPA Voted and clarified; OEM replacement Engine Blocks only for the year Make and Model of the tractor.

Rev. # 4 ~ January 2009 ~ Rules revised and added for2009 & 2010 seasons;  # 2C, # 3A, # 4A, # 5B, # 6F, # 8A,# 9G , #9F, #9I,  # 10, # 10A & # 10B.  TTPA Board Approved 1st Reading 02/21/09 & 2nd Reading 03/19/09.

February 2013 ~ Class approved Rule #2D - NTPA Water & Fuel Rule, #2E – Sample Valve, #3E – Heads for make & Model, #4F – Tach Trigger, #5A – Delete Must have stock Fuel Pump, #5B – 3-way bypass, #6B – 114” Max Wheelbase, #7B – No intercoolers, #7C – Two 3/8” bolts in exhaust, #8A – Factory or better drawbar 3” x 3-3/4” opening, #8D – Hitch height 20”, #9C – No steel fans, #9J – Front Skis, #9K – Reverse Light, #9L – Front Balancer 360° shielding, #9M – Side Shields, #9N – Fiberglass Hoods inner side shielding, #10A –Rear tire sizes, #10B – Delete Front tire size & #11 Rules in place for 1 year post 2013 Pulling Season.  Board Approved 1st Reading ~ 03/16/13 & 04/20/13 ~ 2nd Reading.

2014 Rules ~ No Changes.  Rules in place for 2 years post 2015 Pulling Season.

_____________________________________________________________________________________________Note: This document is not to be copied, revised, used or changed by any other organization other than the, Thumb Tractor Pulling Association Inc. without the written approved / consent of the TTPA Board of Directors.